| Pic Entree | In pic Entrée What does the voltmeter read?_____________- What does a voltmeter measure?___________ Voltage is defined as energy expended per unit charge. How much work will this battery do with the voltage that it shows? |
| --- | --- |
| Pic Crazy Pic Weird | In Pic Crazy The black lead of the voltmeter is made to slide across the wire. What does the voltage in the voltmeter read? ________ This means that there is no voltage drop in the wire. A voltage drop is a decrease in voltage (or energy/charge) along a conductor through which current is flowing. In real circuits, there is a small voltage drop. What does this mean? __________________________________________ __________________________________________ In pic Weird Why does the voltmeter show 0V? Explain using energy concept? __________________________________________- ________________________________________________________________________________________________________________________________________________________________________ |
| Pic Strange | In pic Strange What does the voltmeter read?____________ So the ‘voltage drop’ across the bulb is __V. This means that the entire energy from the cell got used up across the bulb. |

Pic ultimate

In pic ultimate

What does the voltmeter read? Explain using energy concept.

___________________________________

____________________________________ ____________________________________

Voltage, Potential difference and Voltage drop- Potential difference= voltage at each point Voltage= sum of potential differences Voltage/Potential drop-=a decrease in voltage along a conductor through which current is flowing Voltage drop and potential difference can be swapped as their meaning is similar.

Voltage, Potential Difference and Potential drop are used in different sentences.

State if these have been correctly used or not.

A wire has 20 V voltage across it due to a 20 V battery connected at its end points( also called terminal).

___T/F_______

A Wire has a potential difference of 20 V due to a 20 V battery connected across it’s terminals. ___T/F______ A voltmeter measure voltage across a battery._ ____T/F______ A voltmeter measures Potential difference across a battery _____T/F__________ When a voltmeter is connected across any two points in a wire it measures Voltage. _____T/F__________ When a voltmeter is connected across any two points in a wire it measures Potential difference between these two points. _____T/F__________

Write a paragraph summing up the concepts learnt from the above table. The paragraph must explain the concept of energy change when the current flows in the circuit. Take your time; explain as if you are giving details to someone who is relying on you for a better understanding of the Voltage, Potential Difference, and Voltage Drop concept.

# Text boxes

# Understanding Voltage, Potential Difference and Potential /Voltage Drop